## Slide 1: Number Systems & Binary Arithmetic

## Slide 2: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 3: Quantities/Counting (1 of 2)
Decimal | Binary | Octal | Hexa-Decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7

## Slide 4: Quantities/Counting (2 of 2)
Decimal | Binary | Octal | Hexa-Decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 5: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 6: Quick Example
2510 = 110012 = 318 = 1916
Base
Write the base of each number like below:

## Slide 7: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 8: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “position” of the bit starting from 0 on the right
  Add the results

## Slide 9: Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 10: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 11: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the position of the bit, starting from 0 on the right.
  Add the results

## Slide 12: Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 13: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 14: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the position of the bit, starting from 0 on the right.
  Add the results.

## Slide 15: Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 16: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 17: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 18: Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012
Reverse Order

## Slide 19: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 20: Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 21: Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228
Reverse Order

## Slide 22: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 23: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 24: Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4
Reverse Order

## Slide 25: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 26: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 27: Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 28: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 29: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 30: Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 31: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 32: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 33: Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 34: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 35: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 36: Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 37: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 38: Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 39: Example
10768 = ?16
1 0 7 6
001 000 111 110
2 3 E
10768 = 23E16

## Slide 40: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 41: Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 42: Example
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1 7 4 1 4
1F0C16 = 174148
Remove this 0

## Slide 43: Exercise – Convert ...
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 44: Exercise – Convert …
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF
Answer

## Slide 45: Binary Fraction to Decimal
(10.1011)2 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0.0 1 x 21 = 2.0 (2.6875)10
(1011.1001)2 = (?)10

## Slide 46: Octal Fraction to Decimal
(17.53)8 => 7 x 80 = 7.0 1 x 81 = 8.0 5 x 8-1 = 0.625 3 x 8-2 = 0.046875 (15.671875)10
(21.76)8 = (?)10

## Slide 47: Hexa-Decimal Fraction to Decimal
(AB.C1)16 => 11 x 160 = 11.0 10 x 161 = 160.0 12 x 16-1 = 0.75 1 x 16-2 = 0.00390625 (171.7539)10
(8D.EF)16 = (?)10

## Slide 48: Binary Fraction to Octal
100101.0112 = ?8
Partition the binary number into groups of three bits starting from decimal point.
100 101.011
4 5 3
100101.0112 = 45.38

## Slide 49: Binary Fraction to Octal
10101.012 = ?8
Partition the binary number into groups of three bits starting from decimal point.
010 101.010
2 5 2
10101.012 = 25.28
Add this 0 to make three bits

## Slide 50: Binary Fraction to Hexadecimal
01111101.11112 = ?16
Partition the binary number into groups of four bits starting from decimal point.
0111 1101.1111
7 D F
01111101.11112 = 7D.F16

## Slide 51: Binary Fraction to Hexadecimal
111101.1112 = ?16
Partition the binary number into groups of four bits starting from decimal point.
0011 1101.1110
3 D E
111101.1112 = 3D.E16
Add these two 0’s to make four bits

## Slide 52: Decimal Fractions to Binary
3.14579
.14579 x 2 0.29158 x 2 0.58316 x 2 1.16632 x 2 0.33264 x 2 0.66528 x 2 1.33056
etc.
11.001001...
12.51310 = (?)2

## Slide 53: Decimal Fractions to Octal
(5.672)10
5.67210
.672 x 8 5 .376 x 8 3 .008 x 8 0 .064 x 8 0 .512 x 8 4 .096
etc.
(5.53004...)8

## Slide 54: Decimal Fraction to Hexadecimal
15.67210
.672 x 16 10 .752 x 16 12 .032 x 16 0 .512 x 16 8 .192 x 16 3.072
etc.
(F.AC083...)16

## Slide 55: Binary Addition (1 of 2)
Two 1-bit values
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10
“two”

## Slide 56: Binary Addition (2 of 2)
Two n-bit values
  Add individual bits
  Propagate carries
  E.g.,
10101 21 + 11001 + 25 101110 46
1
1

## Slide 57: Multiplication (1 of 3)
Decimal (just for fun)
35 x 105 175 000 35 3675

## Slide 58: Multiplication (2 of 3)
Binary, two 1-bit values
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 59: Multiplication (3 of 3)
Binary, two n-bit values
  As with decimal values
  E.g.,
1110 x 1011 1110 1110 0000 1110 10011010

## Slide 60: Binary Addition Example 1
  1 1 0 1 1 1
  + 0 1 1 1 0 0
1
1
1
1
1
0
1
0
0
1
1
Example 1: Add
binary 110111 to 11100
Col 1) Add 1 + 0 = 1
Write 1
Col 2) Add 1 + 0 = 1
Write 1
Col 3) Add 1 + 1 = 2 (10 in binary)
Write 0, carry 1
Col 4) Add 1+ 0 + 1 = 2
Write 0, carry 1
Col 6) Add 1 + 1 + 0 = 2
Write 0, carry 1
Col 5) Add 1 + 1 + 1 = 3 (11 in binary)
Write 1, carry 1
Col 7) Bring down the carried 1
Write 1

## Slide 61: Binary Addition Verification
Verification
1101112  5510
+0111002 + 2810
  8310
  64 32 16 8 4 2 1
  1 0 1 0 0 1 1
= 64 + 16 + 2 +1
= 8310
  1 1 0 1 1 1
  + 0 1 1 1 0 0
1 0 1 0 0 1 1
You can always check your
answer by converting the figures to decimal, doing the addition, and comparing the answers.

## Slide 62: Binary Addition Example 2
Verification
1110102  5810
+0011112 + 1510
  7310
  64 32 16 8 4 2 1
  1 0 0 1 0 0 1
= 64 + 8 +1
= 7310
  1 1 1 0 1 0
  + 0 0 1 1 1 1
1
1 0 0 1 0 0 1
1
1
Example 2:
Add 1111 to 111010.
1
1

## Slide 63: 1’s Complement of Binary Number
1’s complement: Inverse all bits so that each 1 becomes 0 and each 0 becomes 1.
1 0 0 1
0 1 1 0

## Slide 64: 2’s Complement of Binary Number
1 0 0 1
  0 1 1 0
  + 1
0 1 1 1
2’s complement: Add 1 to the 1’s complement of the binary number.
:9
: -9
2’s complement is the negative representation of the number. That means 01112 is the negative of 10012
1001 = -(0111)

## Slide 65: Binary Subtraction
111-011 = 111+(-011)
Find -011 which is the 2’s complement of 011:
011
100 1’s complement
1
101 2’s complement
Now add 101 and 111:
111
101
1100
So, 111-011 = 100
If we subtract two three numbers result will be in three bits, if we subtract two four bit numbers, result will be in four bits and so on.
Remove extra bit
Verification:
111:7
011:3
7-3=4 which is 100 in binary

## Slide 66: Binary Subtraction
011-111 = 011+(-111)
Find -111 which is the 2’s complement of 111:
111
000 1’s complement
1
001 2’s complement
Now add 001 and 011:
011
001
100
2’s complement the result:
Verification:
011:3
111:7
3-7=-4, How can we verify
that result is -4 or not?
100
011
1
100 :4, that means result 100 is correct.

## Slide 67: Thank You!