## Slide 1: Training Course on ITEE for the Candidates of November 2020 Exam
PROJECT FOR SKILL’S DEVELOPMENT OF ICT ENGINEERS TARGETING JAPANESE MARKET
Solutions
FE PM Questions of October 2015
Question 4
Dr. Md. Nawab Yousuf Ali
Associate Professor, Dept. of CSE
East West University

## Slide 2
Question 4

## Slide 3: Question 4. Read the following description concerning Analog/Digital conversion, and then answer Sub-question.
Pulse Code Modulation (PCM) is a method of converting an analog signal into digital data.
The PCM encoder has three processes:
(1) Sampling → (2) Quantizing → (3) Encoding.
An Analog/Digital conversion of n bits is described below, using the voltage of a direct current as an example:

## Slide 4: Question 4
(1) Sampling
In sampling, a voltage that is a continuous-time analog signal is measured at a fixed time interval.
In Figure 1, the time axis is divided into t0, t1, … at equally-spaced time intervals of d, and the voltage at a given time is represented as v(t0), v(t1), … ..

## Slide 5: Question 4
Figure 1. Example of sampling

## Slide 6: Question 4
(2) Quantization
In quantization, the voltages v(t0), v(t1), … obtained by the sampling in (1) are approximated with integral multiple values of step size q.
In order to perform quantization, first, the FSR, which is the maximum width of the voltage to be measured, is decided.
Next, in order to perform quantization with n bits, step size q is determined by equally dividing the FSR into (2^n − 1) parts. In this case, step size q is FSR / (2^n − 1).
FSR (Force-sensing registor) is a voltage divider setup

## Slide 7: Question 4
(2) Quantization
In quantization, when v0 = 0,v1 = q, …,vmax = (2^n − 1)× q represent the voltage values used as approximate values in ascending order, with regard to the voltage v(tm) of the analog signal measured in sampling at the time tm, a non-negative integer N that satisfies the following condition is found in quantization, and the voltage N × q is taken as the measured voltage v(tm). This is called n bit quantization:
(N × q − q )/ 2 ≤ v(tm) < (N × q + q) / 2

## Slide 8: Question 4
(2) Quantization
As shown on the right in Figure 2, after the voltage axis is divided into voltages v0, v1, …, vmax with step size q, for each of v(t0), v(t1), …, the closest voltage from v0 to vmax is taken as the measured value. For example, the measured value of v(t3) is v2.

## Slide 9: Question 4
Note: “○” is an approximated value of v(tm) in the integral multiples of q
Figure 2. Example of quantization

## Slide 10: Question 4
(3) Encoding
In encoding, the voltages v0, v1, …, vmax used in quantization in (2) are assigned binary codes.
Each measured value is represented using these binary codes.

## Slide 11: Question 4
Subquestion
From the answer groups below, select the correct answer to be inserted in each blank in the following description.
The encoding of the voltages v(t0), v(t1), …, v(t10) as shown on the left in Figure 2 is considered.
Table 1 shows a case where the voltages v0, v1, …, v7 shown on the right in Figure 2 are assigned binary codes 000, 001, …, 111 in sequence.

## Slide 12: Question 4
Subquestion
Table 1. Voltages and corresponding codes
v3 -> 011
v4 -> 100
v5 -> 101
v6 -> 110

## Slide 13: Question 4
Subquestion
Table 2 shows the results when the values measured for v(t0), v(t1), …, v(t10) shown on the left in Figure 2 are encoded in accordance with Table 1.
Table 2. Encoding of values measured at respective times

## Slide 14: Question 4
Subquestion- A, B
Answer group for A and B
a) 011 b) 100 c) 101 d) 110 e) 111

## Slide 15: Question 4
Subquestion- A, B
v3 -> 011
v4 -> 100
v5 -> 101
v6 -> 110
Table 2
Table 1
Table 1
011
111
110
101
011
011
101
v3
v7
v6
v5
v3
v3
v5

## Slide 16: Question 4
Subquestion C
When the voltage range of an analog signal is between 0 and 9V, if the FSR is set to 9V and quantization with 4 bits is performed, q is V.
Here, FSR = 9V and n = 4 bits
We know, step size q is FSR / (2^n − 1)
q= 9/(2^4 -1) = 9/15 = 0.6
So, = 0.6 V
C
C
[FSR is the maximum width of the voltage]

## Slide 17: Question 4
Options for subquestions C and D
Options: a) 0.5625 b) 0.6 c) 1.2 d) 2.25 e) 5.5 f) 7.0 g) 7.2 h) 7.5 i) 7.8 j) 8.0

## Slide 18: Question 4
Subquestion D
The measured value of the voltage 7.49…V of the analog signal is V.
Here, We need to find out the voltage in digital signal when analog signal contain the voltage of 7.49…V .
D

## Slide 19: Question 4
Subquestion D
The measured value of the voltage 7.49…V of the analog signal is V.
We know from quantization, every voltage of digital signal is multiples of step size q.
Vn = (2^n − 1) × q.
So, Options a, d, e, f, h, j are wrong.
Answer will be most nearest value of 7.49 V which is multiples of step size q.
D

## Slide 20: Question 4
Options for subquestions C and D
Options:
0.5625 b) 0.6 c) 1.2 d) 2.25 e) 5.5
f) 7.0 g) 7.2 h) 7.5 i) 7.8 j) 8.0

## Slide 21: Question 4
Subquestion E
When the measured value of is encoded with the binary codes 0000, 0001, …, and 1111 in sequence as in Table 1, the binary code is .
Options: a) 1010 b) 1011 c) 1100
d) 1101 e) 1110
E
D

## Slide 22: Question 4
Subquestion D
The measured value of the voltage 7.49…V of the analog signal is V.
The two nearest value of 7.49 V is option h=7.2 and i=7.8.
But 7.2 is the most nearest than 7.8.
So, measured value is 7.2 V
= 7.2 V
D
D

## Slide 23: Question 4
Subquestion E
When the measured value of is encoded with the binary codes 0000, 0001, …, and 1111 in sequence as in Table 1, the binary code is .
Options: a) 1010 b) 1011 c) 1100
d) 1101 e) 1110
E
D

## Slide 24: Question 4
Subquestion E
Using Vn = (2^n − 1) × q equation, we get-
Voltage | V0 | V1 | V2 | V3 | V4 | V5 | V6 | V7 | V8 | V9 | V10 | V11 | V12 | V13 | V14 | V15
Value | 0 | 0.6 | 1.2 | 1.8 | 2.4 | 3 | 3.6 | 4.2 | 4.8 | 5.4 | 6 | 6.6 | 7.2 | 7.8 | 8.4 | 9

## Slide 25: Question 4
Subquestion E
Using Table-1, we get-
So, =1100
Voltage (V) | Code | Voltage (V) | Code
V0 | 0000 | V8 | 1000
V1 | 0001 | V9 | 1001
V2 | 0010 | V10 | 1010
V3 | 0011 | V11 | 1011
V4 | 0100 | V12 | 1100
V5 | 0101 | V13 | 1101
V6 | 0110 | V14 | 1110
V7 | 0111 | V15 | 1111
E